SCI-DM1031 X-γ dosimeter-radiometer

Purpose of use

- Measurement of personal gamma and X-ray radiation equivalent dose rate(EDR)

- Measurement of personal gamma and X-ray radiation equivalent dose(ED)

- Alarm of exceeded programmed threshold levels

Application

- Environmental protection bureau、public health bureau, inspection and quarantine bureau、radiology department of hospital、 radioaction laboratory、

- Radiation in industrial radiation accelerator and gamma Radiation in industria

- Nuclear power station

- Other radioactive area

Specification

- Measurement ranges:

- Radiation equivalent dose rate:0.01 µSv/h～50mSv/h

- Radiation equivalent dose:0.00 µSv ～9999Sv

- Energy ranges of measurement

- 40Kev～3.0Mev

- Relative errors of energy dependence(137Cs):

- ≤±25%

- Bcsic relative errors:

- ≤±10%

- Adjust able range of alarm threshold level relative to radiation dose rate:

- 0.5 µSv/h -5mSv/h

- Adjust able range of alarm threshold level relative to radiation dose:

- 100uSv-100mSv

- Time of alarm dependence:

- ≤6 sec

- Display unit：

EDR :(µSv/h、mSv/h、Sv/h )

ED:(µSv、mSV、Sv)

- Power supply mode

- One CR123A size battery

- Dimensions：100*60*26 mm

- Weight：90g

Features

- Digital LED display

- Back Light Compensation

- High sensitivity,can measuring environmental background

- Audio and shake looking for and locating radiation source

- Audio and shake alarm of exceeded programmed threshold levels

- Programming of alarm threshold level relative to radiation dose rate and radiation dose

- Programming of the four alarm models:audio、shake、audio and shake、mute

- Low energy consumption

- Display and alarm of electric quantity

- Clock

- Automatic fault detect